## Slide 1
BROOKS mass flow readout
Number | Color | Description | Arduino
1 | Red-blue | Setpoint common | GND
2 | White-green | Flow Signal 0-5 V | A0
5 | Blue | Power Supply +13.5 to +27 VDC | -
8 | Green | Setpoint Signal 0 - 5 V | Pin 9
9 | Gray-brown | Power Supply common | GND
10 | Brown-green | Flow Signal output common | GND
BROOKS
Arduino
Custom cable
Twofast-rpi3-4
USB Serial
Database (twofast-rpi3-0)
LAN cable to network
Table: flow_meter_readout_live
Columns: (time, read_voltage, id)
Every night at 3 AM the flow_meter_readout_live table is appended into the table flow_meter_readout_storage
Readout is started via the script flow_meter_readout_V0.py in ~/Documents/dash_NG/flow_meter/
Use Start_flow_meter_readout.py in LTH_Neutimag\hkromer\17_github\phd_python\01_neutron_generator_control to start script via SSH